## Slide 1: LPS/LDR Data Processing Workshop 10th March 2015
Liz Stanley
Zoe Hall
Albert Koulman
Luke Marney

## Slide 2: Data Processing Workshop (refreshments provided!)
Software requirements
Brief comment on R
Converting files
GitHub repository
DIMS processing using HRMS.R script
  Writing your own lipid-list
  Setting up the processing workflow
  The output
Data post-processing (clean-up procedures)
  Epidemiology studies
  Single plate investigations
LCMS processing using xcms (Zoe)

## Slide 3: Brief comment on R and R studio
There are plenty of books, courses and websites available for R
  R for Dummies is a good place to start
  There are lots of forums, questions and blogs available:
    Quick R at http://www.statmethods.net/
    R bloggers at http://www.r-bloggers.com/
Notes and examples from 2 University of Cambridge courses are available on the LPS Group share at:
  O:\Groups\LPS\Basic_R_courses_Univesity of Cambridge
If you are particularly interested in R, speak to James Smith or Animesh.

## Slide 4: Software requirements
File converter MSCONVERT
  Available from proteowizard
    http://proteowizard.sourceforge.net/downloads.shtml
R and R studio
  R Available from http://www.r-project.org/
  R Studio Available from http://www.rstudio.com/
R packages
  available from http://www.bioconductor.org/
    xcms
    Rcpp
    mzR
    data.table
R scripts and lipid lists
  Updated versions are available on GitHub https://github.com/
  For the purposes of today all scripts and data sets are provided
    O:\Groups\LPS\BioComputing\Data_processing work shop_10Mar2015

## Slide 5: R studio 4 windows
Script
Console
Packages, plots etc
Environment

## Slide 6: R Packages Installation guidelines
data.table (within R)
      install.packages("data.table")
xcms
      source("http://bioconductor.org/biocLite.R")
      biocLite("xcms")
mzR
      source("http://bioconductor.org/biocLite.R")
      biocLite("mzR")
Rcpp
      install.packages("Rcpp")

## Slide 7: Converting files to the .mzXML format - MSConvert
.raw files = input
.mzXML files = output (this is where you will process the data)
MS level 1
1
2
3
4

## Slide 8: Direct infusion spectra (plasma)
Chromatogram
Positive mode
Negative mode
Positive mode
Cholesterol and CE
Cer and SM
TG and DG
Lyso-PC
PC, PE, PA, PS, PI, PG
Negative mode
FFA
Cer and SM
Lyso-PC
PC, PE, PA, PS, PI, PG

## Slide 9: The lipid list (LipidList.csv)

## Slide 10: Setting up the working directory for DIMS processing
Your working directory should contain the following items:
  mzXML files
  HRMS.R script
  HRMS_prompt.R script
  LipidList.csv

## Slide 11: The hrms.R script
Open R Studio and open the hrms_prompt_script

## Slide 12: The hrms.R script Setting up
Step #1 Set your working directory
>setwd(“C:/wd_name”) this is where your mzXML files are stored
Step #2 Source the HRMS.R file
> source(“hrms.R”) loads the HRMS.R processing script
Steps #3 & 4 load the xcms and data.table packages
> library(xcms)
> library(data.table)
(mzR and Rcpp will load automatically with xcms)

## Slide 13: The hrms.R script Processing the 1st spectrum
Step #5 process the 1st spectrum
> main(“filename1.mzXML",rtwin=c(20,60),mzwin=c(200,1200))
The output is a .csv file which contains the following:
  targets.name
  targets.m/z
  nearest_mz
  mz_deviation
  signal
RT window (in seconds)
20-60s for positive mode
80-120s for negative mode
mz window
200-1200 for positive mode
185-1200 for negative mode

## Slide 14: The hrms.R script the .csv file

## Slide 15: The hrms.R script processing all files
Step #6 processing loop for all files
>files = list.files(".", pattern=".mzXML")
system.time(
for (i in 1:length(files)) {
main(files[i], rtwin=c(20,60), mzwin=c(200,1200))
}
)
Produces .csv file for each spectrum

## Slide 16: The hrms.R script producing a data matrix
Step #7 signal and deviation .csv files
>results <- signals_deviations()
Produces 2 .csv files one for signals and a second for deviations
signals
deviations

## Slide 17: Fenland
Fenland Cohort 1
  1500 samples
  19 plates
  4 x 3 QC + 4 blanks on each plate
  96*19 = 1824 runs
  25.5 GB data
Exactive methods
97 bad infusion ( 5.3%)
Data processed using cut-offs
  Signal: 1000
  Coverage: 60%
  De-isotope
Result = 665 variables
Data clean-up 1
AK method
Slide courtesy of AK group talk 05 Nov 2014

## Slide 18: First data clean-up
3 levels QC (level 1: undiluted; 2: 1/1 diluted with PBS, 3: 1/4 dilute with PBS)
For each signal averages across QCs and blank
QC 1 level at least 2x blank level and R2> 0.8
Data clean-up 1
AK method – QCs
Slides courtesy of AK group talk 05 Nov 2014

## Slide 19: Normalisation
After data clean-up: 332 signals
Sum of the intensities of 332 signals determined (total clean signal: TCS)
Average TCS of QC1 determined.
All samples (including QCs and blanks) with TCS lower than average QC1-1.6*SD were omitted
Of the original 1500 samples 1423 remained (95%)
Slide courtesy of AK group talk 05 Nov 2014
Normalisation
AK method

## Slide 20: Data quality
332 signals
Average CV of QC1: 17.0%
Mean CV of QC1: 14.9%
Signals with CV < 25%: 285
Signals with CV < 20%: 236
Data Quality
AK method
Slide courtesy of AK group talk 05 Nov 2014

## Slide 21: Data clean up 2 (ES) Using the deviation data
Pick peaks that lie within a ±5 ppm window of the target mass
Also pick peaks that are present in a certain number (75-90%) of your samples (or pools or QCs if used).
To calculate Dppm =
=IF(AND(pos_dev_ppm!C2>=-5,pos_dev_ppm!C2<=5),LM_plasma_pos_signals!C2,0)
Using the logical commands IF and AND
Only allows the entry of intensity data (clean signals) into a new spreadsheet only if the deviations lie between ±5 ppm

## Slide 22: Data clean up 2 (ES) Data quality and normalistion
In positive mode
  Originally pick 1194 peaks with the lipid list
  Reduced to 180 peaks after clean up (5ppm window, present in 75% of samples)
Data can be normalised:
  To TCS as before
  To standard normal variate (SNV)
    Subtraction of the mean intensity of all variables for each peak
    Followed by division of the standard deviation
      xik = [( xik - `xi ) / Ö(S( xik -`xi )2)] * Ö(K-1)
      Reference: Barnes, R.J., Dhanoa, M.S., and Lister, S.J., (1989), Standard Normal Variate Transformation and De-trending of Near-Infrared Diffuse Reflectance Spectra, Applied Spectroscopy, 43, 772-777.
  To IS (single IS or one for each class)

## Slide 23: Other processing methods for DIMS data
We have another script available for processing DIMS data (Jagpreet Singh)
  This picks all peaks above a pre-set intensity threshold (e.g. 1000)
  There is no automatic assignment function
  Useful script if you suspect you have unknowns or novel lipids
  If you are interested, speak to Albert